## Slide 1
Japan Power Market Review
May 2026 | JEPX structure, Tokyo/Kansai supply shape, fuel proxy screen
Desk read
May screened as a shoulder-season easing month in the sample price data, but the operational read is more nuanced: Tokyo remained more thermal-exposed, while public JEPX stack data showed broad system balance with pockets of thin East/West area-group depth.
System sample avg
21.63
JPY/kWh, May
Tokyo premium
+2.41
JPY/kWh vs Kansai
Stack scarcity
2
System blocks
Tokyo residual
58.6%
Thermal share
Kansai nuclear
28.4%
Generation share
Intraday volume
24.5
GWh/day
Core evidence: processed JEPX offer-stack / intraday data and Tokyo-Kansai generation mix. Fuel, SRMC, futures, and weather are dashboard sample/proxy inputs unless replaced by vendor/uploaded data.
Japan Fuel & Power Market Dashboard | May 2026 report | Public / sample-data screening deck
Generated 2026-06-10

## Slide 2
Scope and Evidence Map
May 1-31, 2026; offer-stack coverage begins May 3 in the processed public cache.
Japan Fuel & Power Market Dashboard | May 2026 report | Public / sample-data screening deck
Generated 2026-06-10
Tier 1: report backbone
JEPX public day-ahead offer-stack depth and regime screens.
JEPX public intraday trade, volume, contract, and range data.
Processed Tokyo/Kansai generation mix, residual thermal, and daily shape.
Use for directional market-structure conclusions.
Tier 2: dashboard proxy context
Sample historical power, fuel, FX, SRMC, and forward curves.
Useful for workflow and relationship testing.
Not settlement-grade marks or a substitute for broker/vendor curves.
Use for caveated screening only.
Tier 3: excluded from hard claims
Participant-level bidding behavior.
Plant-level outage attribution unless linked to verified news/vendor data.
Live order-book or current tradable futures levels.
Flag as future pipeline upgrades.
Sources referenced: JEPX day-ahead/intraday market data, JapanesePower.org regional datasets, OCCTO, METI/ANRE Strategic Energy Plan.

## Slide 3
Executive Summary
Three analyst conclusions from the May dashboard run.
Japan Fuel & Power Market Dashboard | May 2026 report | Public / sample-data screening deck
Generated 2026-06-10
1. System was buffered, not broadly scarce
System offer-stack scarcity flags were limited: 2 scarcity blocks and 84 thin blocks across 4,176 records.
Average system clearing estimate was 14.20 JPY/kWh; average upside depth was 8.6 GW.
Market implication: focus on block-level scarcity, not a blanket May tightness story.
2. Tokyo remained structurally tighter
Tokyo residual thermal share was 58.6% versus Kansai 34.7%.
Tokyo evening thermal ramp averaged 5.8 GW versus Kansai 1.9 GW.
Market implication: Tokyo area premia deserve monitoring into hotter load conditions.
3. Fuel easing was not the whole story
Sample JKM fell -10.2% m/m and CFR Japan coal fell -12.8% m/m.
JEPX system sample averaged 14.5 JPY/kWh above coal SRMC and 10.0 above JKM gas SRMC.
Market implication: use the SRMC screen as a richness flag, then validate with real curves.

## Slide 4
Price and Fuel Screen
Dashboard sample values indicate May fuel easing and softer average power, but these are proxy marks.
Japan Fuel & Power Market Dashboard | May 2026 report | Public / sample-data screening deck
Generated 2026-06-10
JEPX system
21.63
-5.8% m/m
Tokyo
23.89
-5.8% m/m
Kansai
21.49
-5.3% m/m
JKM
12.39
-10.2% m/m
CFR Japan coal
123.4
-12.8% m/m
SRMC richness screen
Coal SRMC
7.13 JPY/kWh
JKM gas SRMC
11.7 JPY/kWh
JEPX system
21.6 JPY/kWh
Screened premium: +14.5 JPY/kWh vs coal SRMC and +10.0 JPY/kWh vs JKM gas SRMC. Treat this as a relationship flag, not a dispatch claim.
Analyst read
May fuel sample data points to lower variable-cost pressure, helped by softer LNG/coal and a firmer yen.
Power averages fell m/m, but Tokyo stayed at a premium to Kansai.
The useful trade question is not simply whether fuel fell, but which hours/areas failed to reprice as stack depth changed.

## Slide 5
Tokyo vs Kansai Supply Shape
Processed monthly generation mix shows a structurally different residual thermal exposure.
Japan Fuel & Power Market Dashboard | May 2026 report | Public / sample-data screening deck
Generated 2026-06-10
Monthly generation share
Tokyo
Gas 48%
Coal 16%
Solar 17%
Kansai
Gas 22%
Coal 16%
Nuclear 28%
Solar 14%
Hydro 12%
Gas
Coal
Nuclear
Solar
Hydro
Biomass
Oil
Wind
Thermal reliance and shape risk
Tokyo residual thermal
58.6%
Kansai residual thermal
34.7%
Tokyo solar midday
38.5%
Kansai solar midday
28.4%
Tokyo evening thermal ramp averaged 5.8 GW versus Kansai 1.9 GW. Kansai also carried 80.3 GWh of renewable curtailment in the processed shape file.
Source: processed Tokyo/Kansai generation monthly, residual thermal, and daily shape tables from JapanesePower.org regional public data.

## Slide 6
JEPX Offer-Stack Read
Ex-post public stack curves show where depth was thin around clearing.
Japan Fuel & Power Market Dashboard | May 2026 report | Public / sample-data screening deck
Generated 2026-06-10
System clearing estimate
14.58
JPY/kWh average
System tightest depth
7.4 GW
Average around clearing
Thin system blocks
2.1%
84 records
Scarcity system blocks
0.04%
2 records
Selected benchmark area groups
System avg clearing
14.6 JPY/kWh
East/Tokyo group
17.8 JPY/kWh
West/Kansai group
11.6 JPY/kWh
East thin share
24.2%
West thin share
20.6%
Market interpretation
System balance was broadly adequate in May, but selected East/Tokyo and West/Kansai-linked area groups showed materially thinner local depth.
Thin-stack flags matter most when they cluster in evening ramp or high-load blocks, because small demand/fuel/weather shocks can move clearing more sharply.
For trading use, pair this view with block-level spreads and intraday convergence rather than treating one daily average as the signal.
Source: JEPX public bidding-curve/price-sensitivity data processed into offer-stack depth and regime screens.

## Slide 7
Intraday Liquidity and Convergence
Processed JEPX intraday data gives the best public read on short-term balancing behavior.
Japan Fuel & Power Market Dashboard | May 2026 report | Public / sample-data screening deck
Generated 2026-06-10
Average price
14.84
JPY/kWh, processed intraday
Daily volume
24.5 GWh
Average May session
Daily contracts
9,953
Average count
High-low range
17.4
JPY/kWh average
Trading read
Healthy intraday volume means convergence signals are more useful than pure screen averages.
Wide block ranges indicate pockets of balancing stress even when daily averages look benign.
Next upgrade: chart block-level spot-intraday spread by hour group and flag repeated late-day divergence.
Data note
The deck uses processed intraday public data for this page. The sample historical table contains a different JEPX intraday average, so it should not be mixed with this public-data metric until the pipeline is reconciled.
Source: JEPX public intraday CSV processed into daily price, volume, contracts, and high-low range summary.

## Slide 8
Weather and Early Summer Setup
May was more a shoulder-season structure month than a heat-load stress month.
Japan Fuel & Power Market Dashboard | May 2026 report | Public / sample-data screening deck
Generated 2026-06-10
Tokyo temp
17.5 C
Average sample weather
Kansai temp
18.9 C
Average sample weather
Tokyo CDD
0.0
Low heat signal
Kansai CDD
6.0
Low heat signal
Why this matters for June-August
May did not yet test summer cooling load, so stack-depth and ramp screens are the better early warning tools.
OCCTO's public materials point to peak-demand/capacity monitoring as the key summer reliability frame.
METI's energy plan reinforces the importance of thermal capacity for balancing renewable volatility, even as Japan targets more renewables and nuclear.
Analyst watchlist
Tokyo evening ramp depth versus weather-normal demand.
Kansai nuclear availability and renewable curtailment risk.
Spot-intraday convergence during high solar and late-day ramp blocks.
Fuel curve repricing if LNG/coal softness reverses.
Sources: dashboard weather proxy, OCCTO public supply-demand role/outlook, METI/ANRE 7th Strategic Energy Plan outline.

## Slide 9
Trading Interpretation
Actionable themes to monitor, without making black-box predictive claims.
Japan Fuel & Power Market Dashboard | May 2026 report | Public / sample-data screening deck
Generated 2026-06-10
Relative value
System price screened rich to fuel SRMC proxies despite softer fuel inputs.
Do not trade the sample SRMC level directly; use it to prioritize spread checks after loading real curves.
Watch for power underreaction if LNG/coal rallies into early summer.
Trader takeaway: validate fuel-to-power transmission with real fuel curves and hour/block power marks.
Regional structure
Tokyo premium persisted and the area is more residual-thermal exposed.
Kansai has more nuclear support, but renewable curtailment and evening ramp still matter.
Monitor Tokyo-Kansai spread against East/West area-stack thinness.
Trader takeaway: regional spread risk should be read through supply shape, not just daily average prices.
Market structure
System offer-stack was mostly balanced, but local thin-stack flags were meaningful.
Intraday range remained wide enough to justify block-level convergence monitoring.
The better signal is a repeated pattern: thin stack + wide intraday range + weather/ramp stress.
Trader takeaway: escalate from daily dashboards to block-level review when those three conditions align.

## Slide 10
Caveats and Upgrade Path
What must be strengthened before this is treated as a production trading pack.
Japan Fuel & Power Market Dashboard | May 2026 report | Public / sample-data screening deck
Generated 2026-06-10
Limitations
Fuel, SRMC, power futures, and forward curves are sample/proxy values unless replaced by uploaded/vendor/broker data.
Offer-stack analytics are ex-post public aggregate curves; they are not participant-level bids or a live order book.
No May 2026 baseload trade-date rows were found in the current processed baseload cache.
News pipeline did not return May rows in the local sample news table.
Highest-value next improvements
Load JSCC/JEPX futures or broker curves for Tokyo/Kansai baseload and peakload.
Add verified plant availability, nuclear restart/outage, and solar/renewables pipeline news tagging.
Reconcile intraday metrics so the sample historical table and processed public table use one definition.
Publish a monthly pack template with automated data confidence flags.

## Slide 11
Sources
Public references and local files used in the May review.
Japan Fuel & Power Market Dashboard | May 2026 report | Public / sample-data screening deck
Generated 2026-06-10
References
JEPX day-ahead market data: public price/volume, bidding curve, price sensitivity, and download pages.
JEPX intraday market data: public intraday price, volume, contracts, and download pages.
JapanesePower.org: public regional half-hourly demand and generation mix archives used by the processed dashboard tables.
OCCTO: public role and supply-demand monitoring context, including system reliability and capacity-market framing.
METI/ANRE 7th Strategic Energy Plan outline: 2040 electricity demand, renewable, nuclear, and thermal policy context.
Local dashboard files: local_metrics_may_2026.json, processed JEPX offer-stack/intraday tables, and Tokyo/Kansai supply mix tables.
This slide deck is a market-intelligence screen, not investment advice and not a settlement-grade price publication.